Persistent sodium channel

Comparison to voltage steps in (Magistretti, 1999)

→ persistent current is well visible
→ decay is much more abrupt in the model
→ traces for higher voltage steps (-40, -35) cut current traces of lower voltages which is not seen in experimental data

With temperature at 36°C

→ no big change compared to 22°C